## Slide 1
EEET2490 - Embedded system: os and interfacing
gROUP aSSigment

## Slide 2
Team member
Kim Nhat Anh
s3978831
Huynh Ngoc Tai
s3978680
Tran Quang Minh
s3988776
Vu Thien Minh Hao
s3938011
Odd
Even

## Slide 3
Project overview
  Build a bare-metal OS for Raspberry Pi
  Implement CLI, screen rendering, and an interactive game
  Main Tasks:
  CLI with commands, history, and auto-completion
  Custom font & display (image/video/text)
  Simple game with UART control and logging

## Slide 4
Task 1: CLI implementation
  ASCII welcome message
  Command prompt (FixingGoodOS>) Supported commands: help, clear, showinfo, baudrate, handshake Command history (-, = keys)
  Auto-complete with Tab
  Live feedback via UART

## Slide 5
Task 1: CLI implementation
CLI Input Flowchart
Split by space → cmd + arg
Loop: Compare cmd with commands
Match
commands[i].cmdFunc(arg)
Print response or update system
Full input buffer
Command Parsing Logic
Idle
ArrowUp
History Index--
ArrowDown
History Index++
Display previous command
Command History

## Slide 6
Task 1: CLI implementation
Feature Group | Command/ Feature | Implementation | Testing (any issues/limitations)
CLI Basic Features | welcome screen | complete | Displays on UART boot
 | help | complete | Shows usage with and without args
 | clear | complete | Clears screen using ANSI codes
 | showinfo | complete | Displays MAC and board revision
 | baudrate | complete | Changes UART0 baudrate live

## Slide 7
Task 1: CLI implementation
CLI Enhancement | OS name in CLI | complete | Static prompt FixingGoodOS>
 | Auto-completion in CLI | complete | Matches prefix and fills input
 | Command history in CLI | complete | Works with “–“ (going back) and “=” (going forward) (We don’t use “-” and ”+” because it would require an extra shift on keyboard)

## Slide 8
Task 2: Font and video display implementation
  Background image with team member names
  Names rendered using custom 8x15 font
  Font System: Derived from Tamzen8x15.bdf
  Parsed and converted into bitmap .h file
  Drawn using drawPixelARGB32()
  Short video rendered frame-by-frame (80 frames, ~10 FPS)

## Slide 9
Task 2: Font and video display implementation
font[ch] (8x15 bitmap)
for each bit
drawPixelARGB32(x, y, color)
char
Font Rendering Flow
video_allArray[]
drawImg video_allArray[i]
wait_msec(100)
videoDisplay()
Video Rendering Logic
pixel_data[]
drawPixelARGB32(x, y, pixel_data[i])
Repeat until finish
drawImg()
Image Rendering Logic

## Slide 10
Task 2: Font and video display implementation
Image, Video, and Text Display | Background image and text display | teamdisplay | Shows names of 4 members in color with the RMIT background.
 | Video display | videodisplay | 80 frames, ~10 FPS

## Slide 11
Task 3: Game Implementation - Basketball hoop
Gameplay:
  Move hoop left/right via UART (keys a, d)
  Catch balls = +score, avoid bombs = -score
  Bombs reduce the score
Game stages: 3 levels with time and score goals
Technical Details:
  Collision detection using AABB
  Framebuffer-based sprite rendering
  Logs sent back to CLI via UART

## Slide 12
Task 3: Game Implementation - Basketball hoop
drawBackground
Game Loop
Move Player ← / → (UART)
Start Game
Main Game Loop Flow
Spawn / Update Balls
Collision Detection
Score Update / Effects
Check Score for Stage / Win
tags: NORMAL, SPECIAL, BOMB, ENLARGE, MULTIPLY
NORMAL → score += 10
BOMB → score -= 100
ENLARGE → player.w += offset
SPECIAL -> score += 30
MULTIPLY -> x2 score received
player ↔ ball[n]
GameObject Interaction Diagram

## Slide 13
Task 3: Game Implementation - Basketball hoop
UART Input Handling in Game
ESC pressed
Pause Menu
→ Continue
→ Restart
→ Exit
Running Game
In-Game Menu (FSM)
key == 'a' → player.x -= speed key == 'd' → player.x += speed key == 'p' → pause
char key = uart_getc()

## Slide 14
Overall Conclusion
A
B
C
Low-level hardware interfacing
D
Handling real-time inputs and visual feedback through UART
Improved embedded C design
Custom CLI and rendering pipeline

## Slide 15
DEMO
TIME